## Slide 1
6 Sigma GB Assignment
IVI LD2 Hoang Xuan Huong
Flush height between LCD and
panel main NG
Contents
1. Define
2. Measurement
3. Analyze
4. Improvement
5. Control

## Slide 2
Six Sigma Project Register
Team | IVI LD2
Leader | Dao Cong Sang
Owner | Hoang Xuan Huong
Theme | Model JLR EMA FCD Flush height between LCD and panel main NG |  |  |  | Period | ’25.04.06~’25.06.19 |  | Task team name | IVI LD Mechanic
Six Sigma Project |  | Improvement Goal (Stretch Goal) |  |  |  |  |  | Idea of breaking the limit | 
 |  | Improvement index |  | Current |  | World Best | Goal |  | 
Reduce Flush between LCD and panel main |  | KPI | Defect rate | 500,529 (ppm) |  | NA | 0ppm | - Make ES sample to verify in line - Request supplier modify mold to control height dimension of panel main | 
 |  | ProjectY | Flush -0.4~0 mm | Cpk=0.28 Z=0.84 |  | NA | Cpk ≥1.33 Z=4.5 |  | 
Management Issue (Biz.Issue) |  | Implement Plan (Fast & Strong) |  |  |  |  |  | Task Member | 
This issue has been around for a long time, and the failure rate is very high at 500,529 ppm, so we waste time to rework and rework fee |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | Location | 
 |  |  |  |  |  |  |  | LG Electronics Viet Nam-Hai Phong | 
Qualitative Performance |  | Quantitative Performance |  |  |  |  |  | Neck Point | 
After this theme, I have opportunity and experience make 6 sigma report for green belt. This is the first time I have made a report like this, so I cannot avoid some shortcomings. I look forward to your comments and support. |  | After this theme, I can save loss time: Before defect rate: 500,529 ppm  EST: Loss time and rework fee (70$ - sample price) After defect rate: 0 ppm  Improve issue Total save cost: 70$*500=35000$ |  |  |  |  |  | Dimension not mention in drawing | 
Team | Name | Role
LD | Huong | Leader
SQA | Hieu | Member
ME | Cuong | Member
PE | Vinh | Member
PD | Hoan | Member
 Schedule
Key activity / Output
D : Define issue, Define defect rate, Collect defective sample
M : Gage R&R evaluate equipment and inspector measurement skills
A : Use Fish bones analysis method to find root cause
I : Meeting discuss, make improvement action plan and follow up
C : Verify action on line, Set up quality meeting to control this issue
D
M
A
I
C
6/1
6/15
6/30
7/12
7/30
Task category
□ HW □ SW
■ Mecha □ Current job
Notes: 2

## Slide 3
1.1 Yy break down
Control
Improve
Analyze
Measure
Define
Big Y
Little y2
Flush issue
Gap issue
Assembly issue
Little y1
Mecha defect
Reduce EMA FCD Defect rate
Hardware defect
Sorfware defect
336,467 PPM
837,005 PPM
Decrease defect rate of
JLR EMA FCD
Before
After
6 Sigma assignment
Material defect → return to supplier
Activity
Little y3
Most of hardware issue cause by foreign material inside the set or camera detect wrong position after assembly process, cable, connector need to improve by PE/Supplier
Function issue will be solved by HQ R&D
Asemble issue from material, design of mechanic parts not optimize, that’s why I choose this issue for my 6 sigma assignment.
LD Mec
Seojin supplier
PIC
837,005 PPM
(xx/xxxEA
Jun~Aug Y26)
76.3% 638,634 PPM
15.9% 13,083 PPM
7.8% 65,286 PPM
Appearance issue
6.9% 251 PPM
69.4% 580,882 PPM
59.8% 500,529 PPM
1.6% 80,353 PPM
Vision inspection
OK/NG
Broken pin connector _ check PCBA
4P
Uniformity Function
Black Uniformity value
Improve software
HQ R&D
Press issue
Machine issue
PE
8.0% 500,529 PPM
Function issue
Sleep curent
Improve program
HQ R&D

## Slide 4
1.2 Pareto
Control
Improve
Analyze
Measure
Define
Add pareto
80:20
Giải thích 80%
Item PICxx
MFG xxx

## Slide 5
1.2 Define project Y
To reduce the flush between LCD and Panel main, Project Y is formed :“Flush “
Flush (height) is the distance from the glass surface to the heightest point of the panel main
Flush (height)
Flush
Probe measurement
Control
Improve
Analyze
Measure
Define
Glass
Panel main
Chi tiết
3D

## Slide 6: 1 Preparation of Gage R&R
Equipment: CMM (coordinate measurement machine) Mitoyoto
Resolution: 0.001 mm
Sample Selection:
Type 1: 1 people measure a sample, measure repeat 30 times
Type 2: 3 operators measure 10 samples, measure repeat 3 times (Blind and random)
4. Blind test: The measurer should not know the information of the
sample to be measured, including the specifications.
5. Random: The measuring sequence of the measurer and the sample to be measured and the repetition are determined randomly
Measure System
How to get sample (sampling)
Control
Improve
Analyze
Measure
Define
Model: JLR EMA FCD
Part name: Panel main
A sample which contains the entire spec or the dispersion of the process should be selected
- Normally ± 10 to 20% is recommended, but it should be selected considering the current state of the goods in stock!
- The choice of sample should reflect the state of the process
- Pick NG/OK samples, including sample near spec.
Resolution

## Slide 7: 2 Result of Gage Study
2.1 Type 1 Study
Control
Improve
Analyze
Define
Measure
Date | 18.June.2025 | Equip | CMM | Target | -0.2
Part no | ABA30132601 | ID | IVI-SQA | +TOL | +0.2
Part name | Bracket Mid Assy | Resolution | 0.001mm | -TOL | -0.2
Choose 1 QC member who skill well, measure 1 part 30 times same measure method to verify the measurement system, look at chart,
we see “Resolution: 0.001<5% of Tol ”  Resolution of equipment is OK, Cg, Cgk >1.33 (OK)
Conclusion: Equipment is OK and can use to measure and analysis.
Result:
- StDev: 0.0006
- Tolerance: 0.1
6xStDev (SV): 0.0033
Capability
- Cg: 23.98 > 1.33
Cgk: 23.96> 1.33
Reference Value | -0.049
Operator | Long
Time | Data
1 | -0.049
2 | -0.049
3 | -0.048
4 | -0.049
5 | -0.049
6 | -0.049
7 | -0.049
8 | -0.05
9 | -0.049
10 | -0.049
11 | -0.048
12 | -0.049
13 | -0.049
14 | -0.049
15 | -0.049
16 | -0.049
17 | -0.049
18 | -0.049
19 | -0.051
20 | -0.049
21 | -0.049
22 | -0.049
23 | -0.048
24 | -0.049
25 | -0.049
26 | -0.05
27 | -0.049
28 | -0.049
29 | -0.049
30 | -0.049
Notes: 1. How to process Type I? We need to measure 30 times for one sample which reference value is known
How to choose Sampling? Chọn mẫu như thế nào? Just choose random sample and know the reference value-
1 mẫu ngẫu nhiên biết trước reference value
2. How to get the reference value? Làm sao để có reference value? –
There are two ways: Hai cách:
- First: Use equipment has high precision (accuracy) Sử dụng thiết bị đo chính xác cao.
- Second: Measure one sample 10 times with equipment has high precision then get mean (average) of these measured values. Đo lặp lại part 10 lần với 1 dụng cụ đo chính xác, sau đó lấy trung bình
3. Cg, Cgk là gì? Cg and Cgk are Measuring capacity index of measuring equipment --- Chỉ số năng lực đo đạc của thiết bị đo Tiêu chuẩn: Cg, Cgk >=1.33 4.
Phân biệt giữa Cg vs Cgk? Cg is used when target and data mean are the same, Cgk is used in case target and data mean is not the same.
5. Công thức của Cg &Cgk? Cp and Cpk are called Process Capability. Pp and Ppk are called Process Performance The index takes into consideration the fact that your data is maybe not centered.
How many method to select sample? Simple random Stratified Systematic Cluster Combination Tiêu chuẩn resolution <5% lấy đâu ra? –Based on the standard of GM, Bosch, VDA 5 The acceptance criteria are less than 5% in GM, Bosch, … and less than 10% in AIAG, so the resolution of the instrument is satisfactory. Tolerance=T=USL-LSL %RE=RE/T

## Slide 8: 2 Result of Gage Study
2.2 Type 2 study
Control
Improve
Analyze
Define
Measure
Date | 18.Oct.2024 | Ruler | CMM | Target | 2.7
Part no | ABA30132601 | ID | IVI-SQA | +TOL | +0.05
Part name | Bracket Mid Assy | Resolution | 0.01mm | -TOL | -0.05
P part = 0.000 < 0.05 - OK  The different between parts is significant
 Since we selected 10 different parts, each part should be different
P operator = 0.650 > 0.05
 It is normal that measurements should not be measured differently.
P part * operator = 0.413> 0.05
 It is normal that Interaction between Part and Operator not occur
which means that the measurement is not different between part & operator
Conclusion:
*3 people measure 10 samples, measure repeat 3 times (Blind and random)
% Study Var (SV) : 1.72 < 10%  OK
 Can use to check process variation.
% Tolerance (SV / Toler) : 2.47 % < 10%  OK
 Can use to judge OK/NG
NDC: 81 > 5  OK
 | Huong |  |  | Long |  |  | Phuc |  | 
 | Time 1 | Time 2 | Time 3 | Time 1 | Time 2 | Time 3 | Time 1 | Time 2 | Time 3
1 | 0.024 | 0.024 | 0.024 | 0.024 | 0.024 | 0.025 | 0.024 | 0.025 | 0.024
2 | -0.002 | -0.002 | -0.001 | -0.002 | -0.002 | -0.003 | -0.002 | -0.002 | -0.002
3 | 0.022 | 0.022 | 0.022 | 0.023 | 0.022 | 0.023 | 0.022 | 0.023 | 0.022
4 | 0.024 | 0.024 | 0.024 | 0.024 | 0.024 | 0.025 | 0.024 | 0.025 | 0.024
5 | -0.022 | -0.022 | -0.021 | -0.022 | -0.022 | -0.022 | -0.022 | -0.022 | -0.022
6 | 0.022 | 0.022 | 0.022 | 0.023 | 0.022 | 0.023 | 0.022 | 0.023 | 0.022
7 | 0.027 | 0.027 | 0.028 | 0.027 | 0.028 | 0.027 | 0.027 | 0.027 | 0.027
8 | 0.021 | 0.021 | 0.021 | 0.021 | 0.021 | 0.022 | 0.021 | 0.021 | 0.021
9 | 0.073 | 0.073 | 0.073 | 0.073 | 0.072 | 0.073 | 0.073 | 0.073 | 0.073
10 | 0.018 | 0.018 | 0.018 | 0.018 | 0.018 | 0.018 | 0.018 | 0.018 | 0.018
Notes: StartQuality toolGage studyGage run chart

## Slide 9
2.2 Type 2 study
Control
Improve
Analyze
Define
Measure
Conclusion:
Based on interaction between samples and inspector, we cannot see significant differences between 10 samples.
Inspector’s skill is acceptable. There is no significant differences between 3 operators during each measurement time.
2 Result of Gage Study

## Slide 10: 2 Result of Gage Study
Issue Name: Flush data
Spec: -0.4 ~ 0mm
Inspection Period: 01-06-2025 ~ 30-06-2025
Sampling method :
Rational sub group sampling
5ea/line /day/at LG line
2.3 Xbar-R Chart Review
Control
Improve
Analyze
Define
Measure
Date | Sample 1 | Sample 2 | Sample 3 | Sample 4 | Sample 5
1-Jun | -0.12 | 0 | -0.06 | 0.01 | -0.07
2-Jun | 0.01 | -0.11 | 0.03 | 0.02 | -0.04
3-Jun | -0.01 | -0.05 | 0.03 | -0.04 | 0.06
4-Jun | -0.04 | -0.05 | -0.07 | -0.09 | -0.12
5-Jun | -0.11 | -0.03 | 0.04 | -0.05 | -0.07
6-Jun | -0.1 | -0.02 | -0.09 | 0 | -0.14
7-Jun | -0.02 | -0.05 | -0.04 | -0.04 | -0.09
8-Jun | 0 | -0.01 | 0.03 | -0.04 | -0.08
9-Jun | 0.01 | -0.05 | -0.07 | -0.11 | -0.06
10-Jun | -0.02 | -0.03 | 0 | 0.04 | -0.05
Conclusion:
- Based on X-bar R- chart result we can see process is stable
Notes: Variances are subject to quality control and improvements !!!
1. How to process Type I? We need to measure 30 times for one sample which reference value is known
How to choose Sampling? Chọn mẫu như thế nào? Just choose random sample and know the reference value-
1 mẫu ngẫu nhiên biết trước reference value
2. How to get the reference value? Làm sao để có reference value?
There are two ways: Hai cách:
- First: Use equipment has high precision (accuracy) Sử dụng thiết bị đo chính xác cao.
- Second: Measure one sample 10 times with equipment has high precision then get mean (average) of these measured values. Đo lặp lại part 10 lần với 1 dụng cụ đo chính xác, sau đó lấy trung bình
3. Cg, Cgk là gì? Cg and Cgk are Measuring capacity index of measuring equipment --- Chỉ số năng lực đo đạc của thiết bị đo Tiêu chuẩn: Cg, Cgk >=1.33 4.
Phân biệt giữa Cg vs Cgk? Cg is used when target and data mean are the same, Cgk is used in case target and data mean is not the same.
5. Công thức của Cg &Cgk? Cp and Cpk are called Process Capability. Pp and Ppk are called Process Performance The index takes into consideration the fact that your data is maybe not centered.
How many method to select sample? Simple random Stratified Systematic Cluster Combination Tiêu chuẩn resolution <5% lấy đâu ra? –Based on the standard of GM, Bosch, VDA 5 The acceptance criteria are less than 5% in GM, Bosch, … and less than 10% in AIAG, so the resolution of the instrument is satisfactory. Tolerance=T=USL-LSL %RE=RE/T

## Slide 11
2.4 Result of current Cpk
Control
Improve
Analyze
Define
Measure
Current Cpk
Cpk = 0.28 → Standard >1.33 → NG
Target of improvement
2 Result of Gage Study
Improvement Goals (Practical)
Increase height between LCD and Panel main
(Before improvement) Zst= 0.84  (after improvement) Flawless
⇒ gap betwen height between LCD and Panel main is center value
P-value = 0.628> 0.05  OK
(Data follow a normal distribution)
P-value = 0.628> 0.05  OK
(Data follow a normal distribution)
Current
0.84
Target
4.5
Z level
Current
Defect rate (ppm)
500,00
ppm
Target(Mean)=0(LSL) + 4.5*0.048(std Dev ) = 0.216 (-)
0
Target
Current
-0.039
Target
Mean
0.216

## Slide 12
3.1 Find the Root Cause that making flush issue
Logic tree analysis
Flush NG
Man
Automatic process
Material
Double side tape
LCD
Appearance standard
Working skill
Thickness NG
Panel main
Height dimension NG
Clean surface of LCD
Check DST condition
Check height of panel main
Man is not related
Machine
Method
Pressure force
Pressure machine
Adjust pressure force
Assembly method
Auto matic process
Man is not related
Other function is OK, only Flush is NG
Input set to jig not fully
Not relate to part input


: Potential factor
Control
Improve
Define
Measure
Analyze


In order to define root cause and improvement action, I use logic tree to find the root cause.

## Slide 13
3.1 Find the root cause that making flush issue
: Potential factor

2 Samples T test
Control
Improve
Measure
Define
Analyze
No | Potential Factors | What is looking for ? | Tool to identify
1 | Panel main | Flush value change when change height of panel main (2.70 → 2.90 mm) | 2 sample T test
2 | Machine | Flush value change when change Fressing force change (75kgf→ 80kgf) | 2 sample T test
3 | Double side tape | Flush value change when change double side tape attached position | 2 sample T test
Notes: Ghi thông số

## Slide 14
3.1 Find the root cause that making flush issue
Control
Improve
Measure
Define
Analyze
2 Samples T _ Analysis
Since the P-Value before and after the changing pressure force are normally distributed
Since the P-Value value is greater than 0.05, the variances of the two data cannot be considered homogeneous _ they cannot be considered different from each other
Check pressure force value before/after change height of panel main (75kgf.cm2 →80kgf.cm2)
H0: Changing the pressure force of machine not effect to flush
H1: Changing the pressure force of machine effect to flush

## Slide 15
: Potential factor

Control
Improve
Measure
Define
Analyze
2 Samples T _ Analysis
Check flush value before/after change height of panel main 2.72mm → 2.90mm
H0: Changing the height of panel main not effect to flush
H1: Changing the height of panel effect to flush
Since the P-Value value is less than 0.05, the variances of the two data can be considered homogeneous _ they can be considered different from each other
Since the P-Value before and after the changing pressure force are normally distributed
3.1 Find the root cause that making flush issue

## Slide 16
Control
Improve
Measure
Define
Analyze
2 Samples T _ Analysis
Check flush value before/after change height of panel main
H0: Changing the tape position not effect to flush
H1: Changing the tape position effect to flush
Since the P-Value value is greater than 0.05, the variances of the two data cannot be considered homogeneous _ they cannot be considered different from each other
Since the P-Value before and after the changing pressure force are normally distributed
3.1 Find the root cause that making flush issue

## Slide 17
: Potential factor

Control
Improve
Measure
Define
Analyze
No | Potential Factors | What is looking for ? | Tool to identify
1 | Panel main | Flush value change when change height of panel main | 2 sample T test
2 | Machine | Flush value change when change Fressing force change | 2 sample T test
3 | Double side tape | Flush value change when change double side tape attached position | 2 sample T test

2 Samples T test
3.1 Find the root cause that making flush issue
Conclusion:
After change height of panel main from 2.70 mm to 2.90 mm, mean change from -0.045 to -0.1985 (center value)
→ This factor effect to issue
Notes: Add conclusion

## Slide 18
Before | After
Reduce height of panel main
As is: 2.72
Control
Analyze
Measure
Define
Improve
4.1 Improvement height of panel main
4. Improvement (short term)
Base on flush data after change height of panel main 2.7~3.0mm
→ We can see if height of panel main is 2.9, the flush is center value
→ We will adjust height of panel main to 2.9mm

## Slide 19
Before | After
Control
Analyze
Measure
Define
Improve
Panel main not control
Add spec 2.90 in the drawing
2.90 ±0.05
4.2 Add height dimension on drawing to control
4. Improvement (long term)

## Slide 20
P-value = 0.263> 0.05  OK
(Data follow a normal distribution)
Cpk = 1.54 → Standard: ≥ 1.33 → OK
Good process capability
4. Improvement
Control
Analyze
Measure
Define
Improve
P-value = 0.628> 0.05  OK
(Data follow a normal distribution)
Cpk = 0.28 → Standard: ≥ 1.33 → NG
Lack of process capability
Before
After
4.4 Process Capability review

## Slide 21
4.4 Process Capability review
4. Improvement
Control
Analyze
Measure
Define
Improve
Check the Z short term (best capability of process) and the Z long term (customer’s perspective):
Zshift = Zst – Zlt = 4.67 – 4.60 = 0.07  Z shift < 1.5
 Proper process control management
Z long term : 4.60 ≥ 4.5, Z short term: 4.67 ≥ 4.5
 Technology is OK

## Slide 22
Control
Define
4.5 Conclusion
Analyze
Measure
Improve
4. Improvement
After checking and found out that the height dimension has problems when test sample, we also suspect that the height dimension is the cause of Flush issue
We conducted improving the height dimension by mold modifycation . After that, we also calculated flush data, use Xbar chart to control and Process capability to evaluate result
The result shows that there is no problems with the height dimension after improvement.

## Slide 23
5. Control
Control
Analyze
Measure
Define
Improve
Date | Sample 1 | Sample 2 | Sample 3 | Sample 4 | Sample 5
1-Jul | -0.22 | -0.16 | -0.21 | -0.24 | -0.22
2-Jul | -0.2 | -0.17 | -0.12 | -0.25 | -0.21
3-Jul | -0.17 | -0.16 | -0.19 | -0.17 | -0.22
4-Jul | -0.14 | -0.2 | -0.13 | -0.26 | -0.26
5-Jul | -0.18 | -0.16 | -0.22 | -0.24 | -0.15
6-Jul | -0.22 | -0.23 | -0.21 | -0.25 | -0.29
7-Jul | -0.18 | -0.24 | -0.18 | -0.17 | -0.15
8-Jul | -0.21 | -0.18 | -0.16 | -0.19 | -0.23
9-Jul | -0.11 | -0.15 | -0.18 | -0.18 | -0.15
10-Jul | -0.27 | -0.14 | -0.17 | -0.14 | -0.2
Conclusion:
No abnormality can be found in the Xbar control chart and the R control chart. Therefore, stability is acceptable, the performance of process over time is Good
To monitor the mean and the variation of process after applying improvement and use control chart to monitor process stability over time.
- Sampling method: Rational sub group sampling firsts 5ea/day at production line for 10 days to analyze:
1. Xbar-R Chart Review after improving

## Slide 24
5. Control
Control
Analyze
Measure
Define
Improve
Date | Sample 1 | Sample 2 | Sample 3 | Sample 4 | Sample 5
1-Jul | 2.88 | 2.94 | 2.89 | 2.86 | 2.88
2-Jul | 2.9 | 2.93 | 2.98 | 2.85 | 2.89
3-Jul | 2.93 | 2.94 | 2.91 | 2.93 | 2.88
4-Jul | 2.96 | 2.9 | 2.97 | 2.84 | 2.84
5-Jul | 2.92 | 2.94 | 2.88 | 2.86 | 2.95
6-Jul | 2.88 | 2.87 | 2.89 | 2.85 | 2.81
7-Jul | 2.92 | 2.86 | 2.92 | 2.93 | 2.95
8-Jul | 2.89 | 2.92 | 2.94 | 2.91 | 2.87
9-Jul | 2.99 | 2.95 | 2.92 | 2.92 | 2.95
10-Jul | 2.83 | 2.96 | 2.93 | 2.96 | 2.9
Conclusion:
No abnormality can be found in the Xbar control chart and the R control chart. Therefore, stability is acceptable, the performance of process over time is Good
To monitor the mean and the variation of process after applying improvement and use control chart to monitor process stability over time.
- Sampling method: Rational sub group sampling firsts 5ea/day at production line for 10 days to analyze:
2. Xbar-R Chart Review after improving the measurement system

## Slide 25
Analyze
Measure
Define
Improve
Control
2. Future plan
Management plan
Supplier add height dimension to control after completed painting process(update on PPAP document)

## Slide 26
1.Result of project
Quantitative Performance (Compare with target)
Qualitative Performance(Compare with target)
Analyze
Measure
Define
Improve
Control
1. Improve issue completely, no more same defect happens
2. Lesson learn, update in issue list, review when new similar project in development to prevent similar defect of other models in advance
Height/Flush Defect Rate (ea)
Before
After
↓100%
(June)
Model: JLR EMA FCD
Part name: Control height of panel main
Before defect rate: 500,529 ppm
 EST: Change new ATO and panel main ( 70$)
After defect rate: 0 ppm  Improve issue
Total save cost= 70$ * 500 EA= 35000 $
NG
OK
Summary Defect rate of EMA FCD after improvement
Chart: Flush defect rate
| 15.May | 18.May | 22.May | 12.June | 16.June | 18.June
Total NG | 50 | 20 | 12 | 0 | 0 | 0
Prod Q'ty | 138 | 47 | 60 | 20 | 30 | 200
Defect rate (ppm) | 362318.8406 | 425531.9149 | 200000 | 0 | 0 | 0
 | Before |  |  | After |  | 
Date | 15.May | 18.May | 22.May | 12.June | 16.June | 18.June
Total NG | 50 | 20 | 12 | 0 | 0 | 0
Prod Q'ty | 138 | 47 | 60 | 20 | 30 | 200
Defect rate (ppm) | 362,319 | 425,532 | 200,000 | 0 | 0 | 0