## Slide 1
LGE Internal Use Only
Understanding Cybersecurity Management System
(UNECE R155, ISO/SAE 21434)
Cyber Security Governance Unit

## Slide 2
LGE Internal Use Only
Background of UNECE R155 enactment
Understanding Cybersecurity Management System (CSMS) based on ISO/SAE 21434
  Organizational Cybersecurity Management [Clause 5]
  Project Dependent Cybersecurity Management [Clause 6]
  Distributed Cybersecurity Activities [Clause 7]
  Concept [Clause 9]
  Product Development [Clause 10]
  Cybersecurity Validation [Clause 11]
  Production [Clause 12]
  Operations and Maintenance [Clause 13]
  End of Cybersecurity Support and Decommissioning [Clause 14]

## Slide 3
LGE Internal Use Only

## Slide 4
LGE Internal Use Only
Security risks that threaten autonomous and connected vehicles.
Attacks on Smart Remote Keys Attacks on Cloud-Based Networks Malware Attacks – Software Security Sensors
GPS / LiDAR (Light Detection and Ranging) / IMU (Inertial Measurement Unit)
Network Attacks
V2X Network Attack
V2V Network Attack
V2I Network Attack
APT (Advanced Persistent Threat) Attack
Engine Control Unit
OBD Port-based attack
Malicious code exploits can cause real physical harm to car passenger and users

## Slide 5: The number of cyber-attacks on smart mobility has increased by 7x within 3 years
LGE Internal Use Only

## Slide 6
LGE Internal Use Only
Enactment background of UNECE WP.29 R155
  As electronic control devices increase in automobiles and connected to communication, cybersecurity vulnerabilities and threats such as illegal control of automobiles and infringement of privacy have been increased.
  The damage to hacking, such as cyber attacks on automobiles, can lead to critical impact on road users that's why
cybersecurity is essential.
UNECE WP.29 R155, the first international standard for automobile cybersecurity, was adopted based on international consensus on the importance of car cyber security on Jan 2021.
12th UN, Informal Working Group on Cybersecurity & OTA (2018, Seoul)
In the European Union, the new regulation on cybersecurity (UNECE WP.29/R155) will be mandatory for all new vehicle types from July 2022 and will become mandatory for all vehicles produced from July 2024

## Slide 7
LGE Internal Use Only
UN *United Nations | 
UNECE *United Nations Economic Commission For Europe | 
…
ITC
*Inland Transport Committee
WP 29
*World Forum For Harmonization Of Vehicle Regulations
…
GRVA
*Working Party on Automated/Autonomous and Connected Vehicles
…
…
…
…
Organization structure
CSMS
(Cybersecurity Management System)
UNECE : One of the five regional commissions under the jurisdiction of the United Nations Economic and Social Council. (56 members states)
WP29 : Unique worldwide regulatory forum within the institutional framework of the UNECE Inland Transport Committee.
UNECE WP.29 enacted the Cyber Security Management System (CSMS).

## Slide 8
LGE Internal Use Only
Applicable to : Passenger cars, commercial vehicles, trailers with electronic control systems, and small vehicles with autonomous driving functions, related automobile manufacturers, etc.
Key takeaways: Manufacturers must have a vehicle cybersecurity management system (CSMS) and conduct risk assessment and management for each vehicle type.
Annex 5 : List of threats and corresponding mitigations
  Part A. Vulnerability or attack method related to the threats
  Part B. Mitigations to the threats intended for vehicles

## Slide 9
LGE Internal Use Only
ISO/SAE 21434 supports to implement a CSMS as it is required by UNECE R155
ISO/SAE 21434 only describes the tasks for a process, but leaves the design to the users
Regulation
ISO/SAE 21434
Standard
Provides guideline how to implement a CSMS
  (Clause 5) Organizational cybersecurity management
  (Clause 6) Project dependent cybersecurity management
  (Clause 7) Distributed cybersecurity activities
  (Clause 8) Continuous cybersecurity activities
….
UNECE WP29 R155
Requires CSMS at high level
  (7.2) Requirements for the Cyber Security Management System
  (7.2.1) For the assessment the Approval Authority or its Technical Service shall verify
that the vehicle manufacturer has a Cyber Security Management System in place and shall verify its compliance with this Regulation.
….

## Slide 10
LGE Internal Use Only
In a secure system of the OEM, all components of the Tiers need to be secure
UNECE R155 has to be applied for homologation from 2024-07-01
on
OEMs need to obtain a valid Cyber Security Management System (CSMS), “Certificate of Compliance”
ISO/SAE 21434 concretizes the requirements of UNECE R155 and is therefore used for an audit
OEM
Tier
Tiers are excluded from UNECE R155, but…
OEMs can require a CSMS certificate
ISO/SAE 21434 will be relevant for Tiers
Establish CSMS
must obtain CSMS certification
Apply cybersecurity to vehicle according to CSMS
must obtain VTA
*VTA : Vehicle Type Approval
Establish CSMS
(Optional) obtain CSMS certification
Apply cybersecurity to products according to CSMS
provide supporting documentation to help OEMs obtain VTA
Tier shall ensure that product development is conducted to ensure cybersecurity compliance based on the ISO/SAE 21434 standard and shall submit and retain all deliverables required by the standard to enable OEMs to obtain a VTA.

## Slide 11
LGE Internal Use Only

## Slide 12
LGE Internal Use Only
Cybersecurity is the collection of measures that can be used to protect the assets

## Slide 13
LGE Internal Use Only
Specifies engineering requirements for cybersecurity risk management regarding concept, product development, production, operation, maintenance and decommissioning of electrical and electronic (E/E) systems in road vehicles, including their components and interfaces.

## Slide 14: Organizational cybersecurity management
LGE Internal Use Only
Project Dependent cybersecurity management
Distributed cybersecurity activities
Cybersecurity validation
Integration / Security
Testing
Implementation
Operations and maintenance
End of cybersecurity support & decommissioning
Concept phase
Risk analysis
Design
Requirement specification
Validation

## Slide 15
LGE Internal Use Only

## Slide 16
LGE Internal Use Only
Organization shall institute and maintain cybersecurity governance and cybersecurity culture, including cybersecurity
awareness management, competence management and continuous improvement to enable cybersecurity engineering
Organizational measures have to be in place to protect the assets and are applied in a defense-in-depth approach
Cybersecurity governance
Cybersecurity policy
Rules and processes
Existing management system
Cybersecurity culture
Continuous improvement
Organizational audits
Risk acceptance
Organizational Measures
Intellectual Property Rights (IPR)
Financial goods
Confidential data
Controlled processes
Cryptographic keys
Reputation
Assets
Protect

## Slide 17
LGE Internal Use Only
The set of policies, processes, and procedures including responsibility & resources that an organization uses to manage and
protect its information assets from cyber threats
Cybersecurity policy
Cybersecurity rules
and processes
Cybersecurity
responsibility
Cybersecurity
resources
enforced by
enabled by
enabled by

## Slide 18
LGE Internal Use Only
The basis for the implementation of ISO/SAE 21434
Cybersecurity policy includes
  Acknowledgement of road vehicle cybersecurity risk
  Executive management’s commitment to manage the corresponding cybersecurity risks
General Organization
Support the awareness of road vehicle cybersecurity risks
OEM Management
Commitment to take care about the risks
Definition of the cybersecurity management scope
External stakeholders
(e.g. third party supplier, end customer)
Support harmonized interface to the OEMs policy

## Slide 19
LGE Internal Use Only
Cybersecurity interests shall interact with the existing management system
Adoption of cybersecurity to the existing processes throughout the complete lifecycle
  Concept, product development, production, operation, maintenance, decommissioning
LG VS CSMS Process

## Slide 20
LGE Internal Use Only
Clear definition of roles and responsibilities
  E.g. Project Manager / Cybersecurity Manager / Vulnerability Tester / Incident Response Manager
e.g)
Role | Responsibility | Required Expertise | Remarks
Cybersecurity manager | Cyber security project management Establish and manage cybersecurity policy Create and manage cybersecurity plans Monitoring and coordinating cybersecurity status and risk/issue Report and escalation cybersecurity key issues or risk Support and coordination cybersecurity issues with Buyer Plan and prepare audit/assessment Manage cybersecurity case | 3 years experience in cybersecurity | Should be a different person with Functional Safety Manager
Personnel assigned to security-related processes shall hold relevant competence being gained by training, experience, seminars, conferences, certifications
  Unexperienced personnel needs to be supervised
Resources should be managed with appropriate tools
  E.g MS Project for WBS, ..

## Slide 21
LGE Internal Use Only
Organization shall foster and maintain a strong cybersecurity culture
Cybersecurity culture generates a common understanding about what cybersecurity means within the company
Awareness of cybersecurity culture can be achieved by training, internal project reviews, lessens learned, lifecycle assessment by external or internal auditor, peer assessment
Evidence can be provided by records of trainings, assessment reports, audit reports
Competence
Cybersecurity culture
Continuous improvement
Awareness

## Slide 22
LGE Internal Use Only
“Need to know” base
To share information can be based on:
  Types of information that can be shared
  Approval processes for sharing
  Requirements for redacting information
  Rules for source attribution
  Types of communications for specific parties
  Vulnerability disclosure procedure
  Requirements for receiving party on handling for highly sensitive information
Information
Documents
Templates
Mail communication
Process descriptions
Project data
HW & SW IPRs
Change history
Personal data
Test results
Documentation
Internal
External
Press release
Authority related
Market
Research results
Market strategies
Customer data

## Slide 23
LGE Internal Use Only
Cybersecurity audit shall be performed independently to judge whether the organizational processes achieve ISO/SAE 21434
(CSMS)
Persons that perform the audit can be internal or external to the organization
Performed periodically to improve process (OEM may require process evidence from suppliers in the supply chain)

## Slide 24
LGE Internal Use Only

## Slide 25
LGE Internal Use Only
Regarding the management of cybersecurity development activities for a specific project
The objectives of this clause
  Assign the responsibilities regarding the project’s cybersecurity activities
  Plan the cybersecurity activities
  Create cybersecurity case
  Perform cybersecurity assessment
  Release for post development

## Slide 26
LGE Internal Use Only
Cybersecurity planning has to be integrated and synchronized with the existing project planning
Contents of cybersecurity plan
  Defines
    Objective of each cybersecurity activity
    Scope and dependencies on other activities or information
    Tailored cybersecurity activities
  Assignment of personnel and responsibilities to roles
  Required resources for performing an activity
  Starting point or end point, and the expected duration of an activity
  Development and implementation of the security requirements
  Verification and validation activities (CAL dependent methods)
  Identification of the work products to be produced
Plus, all activity plan for product life cycle

## Slide 27
LGE Internal Use Only
For each cybersecurity activity a responsible person must be assigned
The responsible person must be competent for the assigned task
Persons are assigned to roles, defined in organizational cybersecurity management
Important part of the cybersecurity plan
e.g)
Name | Role | Company/Department | Expertise, Competences, Remarks | Contact
XXX | Cybersecurit y manager | Cyber Security Management Unit | 10 years experience in cybersecurity management ISO 21434 experience in various project | • +82 … xxx#@lge.com

## Slide 28
LGE Internal Use Only
Rationale must be provided for each tailoring :
  The activity has been omitted or
  The activity is performed in a different manner than previously described
*Activities which are performed by another entity are not seen as tailored
Rationales for tailored processes are also work products (one of evidence for cybersecurity assessment)
e.g)
Definition of item and Cybersecurity goals
Specification of Cybersecurity requirements & Concept
Specification of architectural design
Development of Design
Verification
Definition of the Item
Determination of Cybersecurity Goals
High Level Requirements
Definition of Cybersecurity Concept
Hardware Requirements
Definition of Interfaces
Software Requirements
Definition of Hardware
Architecture
Definition of Software
Architecture
Development / Extension of Hardware Design
Development of Software
Vulnerability Testing
Fuzz Test
Penetration Test
Activity is omitted.
HW architectural design is not necessary due to simple design

## Slide 29
LGE Internal Use Only
Reuse here is the usage of an existing component with respect to cybersecurity functionalities
What is definition criteria of “Reuse of a component”??
  Criteria : SW Change should be under 10% ??, No operational environment change??
Component Name | Related Requirement (ID) | SW Modification (Y/N) | Detail of SW Change (%) - Guide : Synchroniztion rate (over 90%) | Modification of Operational Environment (Y/N) | Detail of Operational Environement change '- OS / Chipset / NW Interface (Ethernet to CAN) Gas <-> Electric Car Etc | Influence on other modules (Y/N)
Asset change (Y/N) | Asset name modifed (Add/delete) | Threat scenario changed (Y/N) | Details of Modifed thrat scenario (Before / After) | Damage scenario changed (Y/N) | Details of Modifed damage scenario (Before / After) | Review result in overall impact analysis

## Slide 30
LGE Internal Use Only
Component Out of Context is the usage of a component which is developed without a specific target application by a third party
and provides cybersecurity features
Component Name | Related Requirement (ID) | Vendor name | Details of assumptions on intended use/context with component feature | related work products | Missing work product / work product to be modified
Details of cybersecurity claims | Dtails of impact on the function behavior | Cybersecurity Interface Agreement (Y/N)

## Slide 31
LGE Internal Use Only
An Off-the-Shelf Component is a mass market product that might not be designed for specific requirements of vehicle
cybersecurity
Component Name | Related Requirement (ID) | Vendor name | Version Name | Influence on other modules and the cybersecurity context (Y/N) | Details of influence on other modues and the cybersecurity context | Definition of implementation datails | Applicabiilty to the existing activities
OSSVS - Availiability of vulnerability test | EM - Availiability of vulnerability test | SCA - Availiability of vulnerability test | Related work product | Missing work product / work product to be modified | Detial of impact on the functional behavior

## Slide 32
LGE Internal Use Only
Security arguments
The Cybersecurity Case shall be created to provide the argument, supported by work products, for the achieved degree of
cybersecurity
Security goals and related cybersecurity arguments
Design analysis
ISO 21434 work products
Test results
Code Analysis reports
Etc…
Provide arguments to claim that
The cybersecurity requirements are met
The cybersecurity functions / measures are implemented
The necessary cybersecurity integrity has been achieved
Evaluation of whether the work products referenced in the
cybersecurity case :
Are traceable from one to another
Have no contradictions within or between work products
Have no open issues
The Cybersecurity Case is summary of the cybersecurity related activities including results
A security argument link the supporting evidence with the overall Security Goals of the item.
It is necessary to provide process and product argument. Usually done in office tools such as Word, Excel

## Slide 33
LGE Internal Use Only
The scope of a cybersecurity assessment :
  Cybersecurity plan and all work products identified in the cybersecurity plan
  Treatment of the cybersecurity risks
  Appropriateness and effectiveness of implemented cybersecurity controls and cybersecurity activities performed for the
project (can be judged by using prior reviews that were performed for verification purposes)
  The rationales, if provided, that demonstrate the achievement of the objectives of ISO 21434

## Slide 34
LGE Internal Use Only
Cybersecurity Assessment must be performed prior to post-development release
If the cybersecurity assessment is not performed, the rationale must be reviewed independently and documented in the cybersecurity case
  Rationale : TARA results / Item, component complexity / process-defined criteria
Cybersecurity assessment can be :
  Performed in incremental steps to facilitate an early resolution of identified issues
  Repeated or supplemented, e.g. due to a change, when a previous cybersecurity assessment provided a negative recommendation, or when a vulnerability is discovered
Person executing the assessment might be from :
  The quality assurance department within the organization
  A different team or department or
  An independent third party
Assessment report shall include a recommendation for acceptance / rejection or conditional acceptance

## Slide 35
LGE Internal Use Only
Release for post-development report is the final statement that the cybersecurity measures have been sufficiently implemented
and the development process has been successfully completed
In case the release is not granted, the criticized activities have to be repeated
Cybersecurity case
Cybersecurity assessment report
Cybersecurity requirements
Argument for the achieved degree of cybersecurity
Supported by work products
Evidence that the cybersecurity requirements are met during the development
Definitions of requirements during post-development
Approved by:
CS Manager Project Lead Assessor
Work product
Release for
post-development
report

## Slide 36
LGE Internal Use Only

## Slide 37
LGE Internal Use Only
Procedure for Distributed cybersecurity activities
  Supplier selection based on record of capability
    Secure production
    Regular cybersecurity training
    Previous Assessment Report
    CSMS certification, etc..
  Request for Quotation
    Cybersecurity goals,set of cybersecurity requirements / Expectation of CIA / Request to conform ISO 21434
  Cybersecurity Interface Agreement (CIA)
Proposed Implementation
Specification
Proposed Implementation
Specification
What do I want?
What can I provide?
What do I want?
What can I provide?

## Slide 38
LGE Internal Use Only
A customer and a supplier shall specify the distributed cybersecurity activities in a cybersecurity interface agreement
CIA including :
  Appointment of customer’s and supplier’s points of contact regarding cybersecurity
  Identification of cybersecurity activities that are to be performed by customer and supplier
  Information and work products to be shared
  Milestones regarding the distributed cybersecurity activities
  Definition of the end of cybersecurity support for the item or component
R : Responsible A : Accountable S : Support
I : Inform C : Consult
Who is responsible? Who do I talk to?
What if problems occur?
What is my task?
What are the milestones?
How do we exchange information (securely)?

## Slide 39
LGE Internal Use Only

## Slide 40
LGE Internal Use Only
Objectives of Concept
  Define the item, its operational environment and their interactions in the context of cybersecurity
  Specify cybersecurity goals and cybersecurity claims
  Specify the cybersecurity concept to achieve cybersecurity goals
Concept phase activities
  OEM defines functions, security goals and a first architecture
Item
definition
Risk analysis
(TARA)
Cybersecurity
concept

## Slide 41
LGE Internal Use Only
GSM
WIFI
Etc..
USB
BT
CAN
Item Boundary
Trust Boundary
Interfaces
Interaction
Item and Item boundary
GSM
WIFI
Etc..
USB
BT
CAN
Item Boundary
Interfaces
Interaction
Item functions and preliminary architecture
Functions |  | 
Touch | Display | Voice control
Call | Navigation | Playing MP3
WiFi Comm.. | Purchasing App | BT Comm..
Components |  | 
Processor |  | 
Display |  | 
RAM |  | 
… |  | 
Item functions, Item boundary, Preliminary architecture shall be identified
Operational environment shall be described, provides supplemental information for analysis activities of the TARA
Item definition serves as input for the TARA (Threat Analysis and Risk Assessment)
E.g) IVI
Central Gateway
Powertrain / Transmission control
In Vehicle Infotainment System (IVI)
Telematic Unit
Body Control
Safety Chassis Control
CAN
CAN
FlexRay
FlexRay
HS-CAN
Item on vehicle level / Operational Environment

## Slide 42
LGE Internal Use Only
TARA based on the item definition shall be performed that involves :
  Asset identification
  Damage & Threat scenario identification
  Impact rating
  Attack path
  Attack feasibility rating
  Risk value determination
TARA Steps
  TARA is a formalized step-by-step approach, which is essential for any following lifecycle
Item Definition
Asset identification
Damage scenario
Impact rating
Risk value determination
Threat scenario identification
Attack Path analysis
Attack feasibility rating
Risk treatment
decision

## Slide 43
LGE Internal Use Only
Asset : object that has value, or contributes to value
Asset has one or more cybersecurity properties whose compromise can lead to one or more damage scenarios
Or Asset is simply something that needs to be protected by cybersecurity techniques
e.g) Headlamp system
Navigation ECU
Gateway ECU
Bluetooth
Cellular
 |  | Item boundary | 
Headlamp Body switch control ECU Headlamp system |  |  | Power switch actuator
 | CAN |  | 
Headlamp Switch
Considered function:
Use power switch actuator to turn the head lamp OFF and ON
The body control unit sends a message over the CAN bus to the Power Switch Actuator of the Head Lamp
Gateway controls access to the CAN bus for other ECUs
Asset | Confidentiality | Integrity | Availability
Data communication (lamp request) | - | X | X

## Slide 44
LGE Internal Use Only
Damage scenario can include :
  Relation between the functionality of the item and the adverse consequence
  Description of harm to the road user and/or
  Relevant assets
Navigation ECU
Gateway ECU
Bluetooth
Cellular
 |  | Item boundary | 
Headlamp Body switch control ECU Headlamp system |  |  | Power switch actuator
 | CAN |  | 
Asset | Confidentiality | Integrity | Availability | Damage scenario
Data communication (lamp request) | - | - | X | Vehicle cannot be driven at night, because the headlamp function was inhibited while parked.
 | - | X | - | Front collision with a narrow stationary object caused by unintended turning-off of headlamp during night driving at medium speed

## Slide 45
LGE Internal Use Only
Damage scenario | Safety | Financial | Operational | Privacy
Vehicle cannot be driven at night, because the headlamp function was inhibited while parked. | Negligible | Negligible | Major | Negligible
Front collision with a narrow stationary object caused by unintended turning-off of headlamp during night driving at medium speed | Severe | Major | Major | Negligible
Severe
Major
Moderate
Negligible
Impact
Impact rating :
  Assess the damage scenarios against adverse consequences for stakeholders
  Depends on the point of view
*Stakeholder is a person or organization that can be affected by a damage scenario
The following impact categories have at least to be considered :
    Safety impact
      injuries range from life-threatening (severe) to moderate and no injuries (negligible)
    Financial impact
      financial damage from catastrophic (severe) to irrelevant (negligible) to the stakeholder
    Operational impact
      operational damage from not working (severe) to indiscernible (negligible) degradation
    Privacy impact
      privacy from highly sensitive (severe) information to inconveniencies (negligible)
Each damage scenario is assessed regarding Safety, Financial, Operational and Privacy (S,F,O,P) impact which results in four
values

## Slide 46
LGE Internal Use Only
Negative actions need to be identified that lead to a damage scenario in a threat scenario
The identification of threat scenarios :
  Is a result of a team work, not by a single person
  Uses a brainstorming-based approach
STRIDE
…
Front collision with a narrow stationary object caused by unintended turning-off of headlamp during night driving at medium speed
Spoofing : Attacker claims to be body control ECU and sends “Lamp request” signal
Tampering : Attacker modifies “Lamp on” to “Lamp off”
Damage scenario
Threat scenario 1
Threat scenario 2
Threat | Description
Spoofing | Pretending of a false identity
Tampering | Manipulation of data
Repudiation | Denying an illegal action
Information Disclosure | Revealing sensitive information
Denial of Service | Making unavailable to its intended users
Elevation of Privileges | Perform an unauthorized action
STRIDE helps to consider multiple threats from different points of
view.
STRIDE is based on observation and experience.
 Certain threats are more prevalent than others

## Slide 47
LGE Internal Use Only
Identifying steps for the execution of a threat scenario (= attack path)
Threat scenario 1
Spoofing : Attacker claims to be body control ECU and sends “Lamp request” signal
Attacker compromises navigation ECU from cellular interface
Necessary actions for a threat scenario
to become real
Attack Path 1a
Compromised navigation ECU transmits malicious control signals
Attack Path 1b
Gateway ECU forwards malicious signals to power switch actuator
Attack Path 1c
Malicious signals spoof the lamp request (OFF)
Attack Path 1d
Navigation ECU
Gateway ECU
Bluetooth
Cellular
 |  | Item boundary | 
Headlamp Body switch control ECU Headlamp system |  |  | Power switch actuator
 | CAN |  | 

## Slide 48
LGE Internal Use Only
The rating is based on these categories :
  High : (The attack path can be accomplished utilizing) low effort
  Medium : medium effort, Low : high effort, Very low : very high effort
Attacker compromises navigation ECU from cellular interface
Attack Path 1a
Compromised navigation ECU transmits malicious control signals
Attack Path 1b
Gateway ECU forwards malicious signals to power switch actuator
Attack Path 1c
Malicious signals spoof the lamp request (OFF)
Attack Path 1d
= 4+6+7+1+0 = 18  Medium
Attack potential-based approach
Element | Description
Elapsed time | Time to identify a vulnerability and develop and apply an exploit
Expertise | Capabilities of the attacker, relative to their skill and experience
Knowledge of the item | Amount of information the attacker can acquire
Window of opportunity | Discover the target, access to a target, exploit works on the target, time to perform the attack on a target
Equipment | Tools the attacker has available to execute the attack
* Kinds of attack feasibility rating approach
Attack potential-based approach
CVSS-based approach
attack vector-based approach
 Different methods can lead to different results. One method shall be used for the rating of each attack path

## Slide 49
LGE Internal Use Only
 |  | Attack feasibility |  |  | 
 |  | very low | low | medium | high
Impact rating | severe | 2 | 3 | 4 | 5
 | major | 1 | 2 | 3 | 4
 | moderate | 1 | 2 | 2 | 3
 | negligible | 1 | 1 | 1 | 1
Determination of the risk of a threat scenario based from the impact of the associated damage scenario and the attack
feasibility of the associated attack paths
Risk values can be determined utilizing risk matrices defined by the organization
Safety, Financial, Operational, Privacy
Drive risk value on each S,F,O,P
Risk value could be highest value among risk values on Safety, Financial, Operational and Privacy
 |  | Attack feasibility |  |  |  |  | 
 |  | very low | low | medium |  |  | high
Impact rating | severe | 2 | 3 |  | 4 |  | 5
 | major | 1 | 2 |  |  |  | 4
 |  |  |  |  | 3 |  | 
 | moderate | 1 | 2 | 2 |  |  | 3
 | negligible | 1 | 1 |  | 1 |  | 1
Damage scenario | Safety | Financial | Operational | Privacy
Front collision with a narrow stationary object caused by unintended turning-off of headlamp during night driving at medium speed | Severe | Major | Major | Negligible
Risk value
S : 4
F : 3
O : 3
P : 1

## Slide 50
LGE Internal Use Only
For each threat scenario, considering its risk values, risk treatment options could be :
  Avoiding the risk (by removing the risk sources)
  Reducing the risk (e.g. by reducing the factors of the attack feasibility)
  Sharing (Transferring)the risk (e.g. by contracts / insurances)
  Retaining or Accepting the risk
Risk treatment decision might affect the mitigation measure for a threat
Risk treatment according to risk value can be defined by the organization
 |  | Attack feasibility |  |  | 
 |  | very low | low | medium | high
Impact rating | severe | 2 | 3 | 4 | 5
 | major | 1 | 2 | 3 | 4
 | moderate | 1 | 2 | 2 | 3
 | negligible | 1 | 1 | 1 | 1
Safety, Financial, Operational, Privacy
Risk value | Risk treatment option
5 | avoiding the risk / reducing the risk
4 | reducing the risk
3 | reducing the risk
2 | sharing or transferring the risk
1 | accepting or retaining the risk
e.g) Risk treatment option to each risk value

## Slide 51
LGE Internal Use Only
Cybersecurity goals are the top level security requirement
The existence of several cybersecurity goals for one item is possible
One cybersecurity goals can be related to several cybersecurity requirements
Cybersecurity goals are typically defined by the OEM
Risk treatment
Cybersecurity Claim
Cybersecurity Goal
Cybersecurity Monitoring, Vulnerability Management
Cybersecurity Requirement
/ Control
Share, Retain
Reduce
Relation of terms – Cybersecurity Goal
  Fact : Data is stored unencrypted
  Outcome of TARA : loss of privacy is possible (threat), Reduce (risk treatment)
  Security goal : Protection of stored private data
  Security requirement : Private data shall be encrypted
  New asset : Encryption key
Item
TARA
Cybersecurity Goal
Cybersecurity
Requirement
Risk accepted
New asset

## Slide 52
LGE Internal Use Only
Statement about a risk
If risk treatment includes :
  Sharing the risk or
  Retaining and accepting the risk due to one or more assumptions
Then one or more cybersecurity claims shall be specified
Cybersecurity claims can be considered for cybersecurity monitoring
Risk treatment
Cybersecurity Claim
Cybersecurity Goal
Cybersecurity Monitoring, Vulnerability Management
Cybersecurity Requirement
/ Control
Share, Retain
Reduce
Relation of terms – Cybersecurity Claim
  Outcome of TARA : Compromise of library (threat), Share (risk treatment)
  Security claim : If the library is compromised, then the tier and the OEM share the responsibility by contract. The tier is responsible to perform monitoring activities and vulnerability management
 Details of security claims shall be part of Cybersecurity Interface Agreement
Item
TARA
Threat
Cybersecurity
Claim
Monitoring

## Slide 53
LGE Internal Use Only
E.g.1
  “A risk value of 1 is generally accepted because it’s below the acceptance criteria for risks.”
E.g. 2
  “Encryption with algorithm DES is sufficient because the following is assumed:
    Attacker is considered as not be a Proficient and does not have knowledge to exploit DES
    Window of opportunity is low: Algorithm needs to be broken during drive in Bluetooth range
    The ECU does not have the resources to handle and calculate higher sophisticated algorithms
    This claim shall be re-evaluated once a year
Cybersecurity claim is a description of why a risk is acceptable, including a specification under which condition the risk need to be re-evaluated

## Slide 54
LGE Internal Use Only
Cybersecurity Claim
TARA
Risk treatment
Cybersecurity Goal
Assigned/qualified person performs the verification of cybersecurity goals/claims through review
  Are the cybersecurity goals meaningful and aligned with the item definition?
  Is the risk treatment decision aligned with the results of TARA? Is this all consistent?
  Do the cybersecurity goals and claims address the risk treatment decision adequately?
  Are there any conflict between the cybersecurity goals and claims?
= Verification
Item definition

## Slide 55
LGE Internal Use Only
Define technical and/or operational cybersecurity controls
  Cybersecurity control : measure that is modifying the risk
5
1
Risk value :
Risk value :
By applying cybersecurity control, risk value is decreased.
Derive cybersecurity requirements from cybersecurity goals
  What is the specified functionality?
  How are interactions between components specified?
  How are the requirements verified?
  Are there external dependencies, e.g. requirements for other items?
Allocate cybersecurity requirements to the item or its components
Plan the cybersecurity validation to show that cybersecurity goals are achieved
Cybersecurity goals
Derive
Cybersecurity requirements
Allocate
Architectural elements
Verification

## Slide 56
LGE Internal Use Only
All cybersecurity requirements need to be verified to show :
  Consistency with the Cybersecurity Goals
  Consistency with the Cybersecurity Claims
The verification is summarized in a Verification Report
Verification of cybersecurity concept supports the cybersecurity case
Cybersecurity
goals / claims
Cybersecurity Requirements
Derive
Verify
Verification Report
E.g. Cybersecurity concept (Infotainment System)
[…]
  Cybersecurity controls
RQ 4711 : Private data shall be encrypted
RQ 4711.1 : Component shall have sufficient resources to handle encryption RQ 4711.2 : Encryption keys shall be stored securely
  Cybersecurity requirements – operational environment
RQ 4712 : Identification/authentication for Bluetooth connections prior to data exchange RQ 4712.1 : Common Bluetooth standard shall be used
  Allocation to item/components
RQ 4711 – supplier shall select appropriate components
RQ 4712 shall be ensured through “Bluetooth communication” component

## Slide 57
LGE Internal Use Only
Level of rigor that provides confidence that protection of the assets is adequately developed
The CAL is assigned to a cybersecurity goal and is inherited by cybersecurity requirements
Based on the assigned CAL, the rigor of verification activities can be defined
 |  | Attack vector |  |  | 
 |  | Physical | Local | Adjacent | Network
Impact rating | severe | CAL2 | CAL3 | CAL4 | CAL4
 | major | CAL1 | CAL2 | CAL3 | CAL4
 | moderate | CAL1 | CAL1 | CAL2 | CAL3
 | negligible | - | - | - | -
*attack vector-based approach
CS Goal (1)
Test 1:
Test 2:
CS Goal (2)
Test 1:
Test 2:
Test 3:
CAL 2
CAL 3
assign
assign
ISO/SAE 21434, Annex E
*Higher CALS require higher independency of cybersecurity activities

## Slide 58
LGE Internal Use Only

## Slide 59
LGE Internal Use Only
To fulfil cybersecurity concept :
  Define cybersecurity specifications
  Verify that the defined cybersecurity specifications conform to the cybersecurity specifications from higher levels of architectural abstraction
  Identify weakness in the component
  Provide evidence that the results of the implementation and integration of components conform to the cybersecurity specifications
Product Development

## Slide 60
LGE Internal Use Only
One Security Goal is realized by at least one cybersecurity requirement
Function(s)
item
asset
Cybersecurity goal
Cybersecurity
requirements
implements
consist of component
contains
associated with
allocated to
allocated to
protects
realized by
The item’s component (memory) contains the asset “Confidential data?.
The Cybersecurity goal : protect confidential data from unauthorized reading, modification, deletion.
The Cybersecurity goal is realized by the Cybersecurity requirements CySecR0001 : Confidential data shall be encrypted
CySecR0002 : Identification and authorization mechanism shall allow authorized users to read, modify and delete data CySecR0003 : Deletion of confidential data by unauthorized users and processes shall be prevented by MMU. CySecR0004 : ….
Inputs for Security Requirements Specification
Already established cybersecurity controls
Existing architectural design
Cybersecurity Concept
Item Definition
Cybersecurity Specifications
Cybersecurity-related components that are not present in the existing architectural design

## Slide 61
LGE Internal Use Only
The defined cybersecurity requirements shall be allocated to components of the architectural design
Procedures to ensure cybersecurity after the development of the component shall be specified
  E.g. Procedures for correct integration and initialization of cybersecurity controls as well as maintaining cybersecurity throughout production
GSM
WIFI
Etc..
USB
BT
CAN
GSM
WIFI
Power Supply
HSM
Processor
Display
Controller
GPS
NVM
RAM
USB
BT
CAN
Transceiver
The HSM shall store the private key for validation of signed firmware
Symmetric crypto engine of HSM shall be configured to 128 Bit key
Timestamp = GetGPSTimestamp()
WiifPW =
PRNG(timestamp)
WiifPW = PRNG(DEFAULT_TI MESTAMP)
fail
success
The default WiFi-Password shall be calculated by a PRNG based on the GPS-Timestamp when the device is turned on for the firs time in production

## Slide 62
LGE Internal Use Only
If design, modelling or programming notations or languages are used for the cybersecurity specifications or their implementation,
the following shall be considered when selecting such a notation or language
  Unambiguous and comprehensible definition in both syntax and semantics
  Support for achievement of modularity, abstraction and encapsulation
  Support for the use of structured constructs
  Support for the use of secure design and implementation techniques
  Ability to integrate already existing components (e.g. library, framework, software component written in another language)
  Resilience of language against vulnerabilities due to its improper use (e.g. resilience against buffer overflows)
Criteria for suitable design, modelling or programming languages for cybersecurity that are not addressed by the language itself shall be covered by design, modelling and coding guidelines, or by the development environment.
MISRA C:2012
“Guidelines for the use of C language in critical systems”
ISO/IEC TS 17961:2013
“C Secure”
2016 SEI CERT C
Mapping of MISRA C coverage of the "CERT C“ / “C Secure” requirements shows that MISRA C already has excellent coverage of those recommendations.

## Slide 63
LGE Internal Use Only
The architectural design shall be analyzed to identify weaknesses
  Known weaknesses and vulnerabilities from reused components can be considered
  Identified weaknesses can be resolved with change to the architectural design without performing a vulnerability analysis
GSM
WIFI
Etc..
USB
BT
CAN
C
Network stack
Math
Kernel
POSIX
File system
Hardware Abstraction Layer
Hardware
Operating System
Cybersecurity Agency
Alert (AA84-242AA)
BadAlloc vulnerability – CVE-2021-220477
Technical Details
Integer overflow vulnerability affecting the calloc() function in C runtime library Affected product version
Secure OS 1.0
Mitigation
Contact manufactural for patch

## Slide 64
LGE Internal Use Only
The defined cybersecurity specifications shall be verified to ensure completeness, correctness, and consistency with the
cybersecurity specifications from higher levels of architectural abstraction
Verification methods can include :
  Review
  Analysis
  Simulation
  Prototyping

## Slide 65
LGE Internal Use Only
Source code shall :
  be readable and understandable
 compile-time complexity analysis
  result into software which can be tested
 compiler switch dependent test functions
  keep the coding guidelines
 compile-time static analysis
  fulfil all specified requirements
 requirement tracking tool
E.g. for Secure Coding Standards
  SEI CERT C
  CERT C++
  Android Secure
  SEI CERT Oracle (for java)
  SEI CERT Perl
OWASP Secure Coding Practices – Quick Reference Guide
Secure Coding Guidelines for Java SE (Oracle)
Secure Coding Guidelines for .NET Framework
3.5 (Microsoft)
…..

## Slide 66
LGE Internal Use Only
Integration and verification activities shall verify that the implementation and integration of components fulfil the defined
cybersecurity specifications
The integration and verification activities shall be specified considering :
  The defined cybersecurity specifications
  Configurations intended for series production, if applicable
  Sufficient capability to support the functionality specified in the defined cybersecurity specifications
  Conformity with the modelling, design and coding guidelines, if applicable
Methods for verification
  Requirements-based test (Positive and Negative test cases / Support cybersecurity requirements)
  Interface test (Proper functionality / Interoperability / Consistence to interface description)
  Resource usage evaluation (CPU, Memory utilization / Bus communication load / Timing constraints)
  Verification of the control flow and data flow (Input validation / Data flow between components)
  Dynamic analysis (Statement coverage / Branch coverage)
  Static analysis (Support security analysis)
Test cases can be derived from analysis of requirements, generation and analysis of equivalence classes, boundary value analysis and error guessing based on knowledge or experience

## Slide 67
LGE Internal Use Only
Testing should be performed in order to confirm that unidentified weaknesses and vulnerabilities remaining in the component
are minimized
  Unnecessary functionalities can contain weakness
  Testing methods
    functional testing
    vulnerability scanning
    fuzz testing
    penetration testing
If testing is not performed, then a rationale shall be provided
  The rationale can include the following considerations
    feasibility to access the attack surface of the component
    capabilities to (directly or indirectly) access the component in combination with compromise of other components
    simplicity of the component

## Slide 68
LGE Internal Use Only

## Slide 69
LGE Internal Use Only
Cybersecurity validation has to be performed by OEM on vehicle level
  To validate cybersecurity goals/claims
  To confirm the item achieves the cybersecurity goals
  To confirm that no unreasonable risks remains
Rationale for the selection of validation activities shall be provided
  CAL ? / Review of managed risks ? / Operational environment? / Goals, claims? / Penetration test ?

## Slide 70
LGE Internal Use Only
Confirmation of achievement of cybersecurity goals by reviewing the work products of cybersecurity concept & product
development
Penetration testing to demonstrate adequacy and achievement of cybersecurity goals
  It is recommended but penetration test on vehicle level might detect additional vulnerabilities
All managed risks identified during concept and development phase should be taken into consideration
  Review of managed risks
Risk
Controls
Residual Risk
Are cybersecurity controls still effective in operation environment?
Is residual risk accepted on vehicle level?

## Slide 71
LGE Internal Use Only
The validation report is used as evidence for the OEM that the product has been developed securely
  Version of product
  Rational for selection for validation activities
  Summary of validation test results
Vulnerability assessment – Example IVI
Finding xxx :
An attacker can crash IVI functionality by sending invalid data over OBD
Vulnerability analysis
Where does this vulnerability come from?
Vulnerability management
Assessment of risks
Vulnerability elimination
Risk treatment decision
Necessary lifecycle phases have to be repeated until vulnerability is fixed

## Slide 72
LGE Internal Use Only

## Slide 73
LGE Internal Use Only
Objectives
  Apply the cybersecurity requirements for post-development
  Prevent the introduction of vulnerabilities during production
Production control plan including :
  Post-development requirements
  Production tools and equipment
  Cybersecurity controls preventing unauthorized alteration
  Verification methods for cybersecurity requirements for post-development

## Slide 74
LGE Internal Use Only
Cybersecurity post-development requirement
  After production, diagnostic interfaces are no longer needed
  Diagnostic interfaces can be an attack vector, solution could be :
    Sealed hardware plug
    New firmware flash without code to access JTAG
  The privileged account is no longer needed  Remove account
 Avoid any access to the ECU via diagnostic interface and privileged accounts
Production tools and equipment
  List all equipment
    E.g. PCs, PLCs, scanners, printers etc.
  Identify needed tools
    E.g. test tools, flashing software etc.
  Identify versions
 Inventory of used tools and equipment is needed for (secure) production

## Slide 75
LGE Internal Use Only
Cybersecurity controls
  Defense-in-Depth approach to protect sensitive data
  If one layer is bypassed, other layers protect the asset
Training
Encryption
Sensitive data
Access control
Verification of post-development cybersecurity requirements
  Define checks to verify that post-development cybersecurity requirements are met, either
  Check manually that hardware plug protects debug interface
  Automatic with pre-defined test cases :
    To check removal of privileged accounts
    To verify that correct firmware is flashed

## Slide 76
LGE Internal Use Only

## Slide 77
LGE Internal Use Only
Objectives
  Determine and implement remedial actions for cybersecurity incidents
  Maintain cybersecurity during and after updates to items or components after production until their end of cybersecurity support
Cybersecurity information evaluation
Criticality classification “Triage”
Incident Response
Incident Review Team
Incident?
No
Yes
Low
High Medium
Terms
Cybersecurity information :
Information with regard to cybersecurity for which relevance is not yet determined
Cybersecurity incident :
Situation in the field that can involve vulnerability exploit mitigation
Triage :
Analysis to determine the relevance of cybersecurity information to an item or component

## Slide 78
LGE Internal Use Only
Continuously monitoring shall be performed to identify cybersecurity issues as early as possible
Researchers
Public
Authorities
assets
vulnerabilities
forensic data
user complaints
Incident Response Team
Marketing
Sales
QM
Legal
Development
internal
external

## Slide 79
LGE Internal Use Only
Incident Response Process
Cybersecurity event evaluation
Criticality classification “Triage”
Weakness
Incident Response Team
Event?
No
Yes
Low
High
Medium
Vulnerability
Analysis
Cybersecurity Incident Response
Risk treatment
Incident?
Terms
Cybersecurity event :
Cybersecurity information that is relevant for an item or component
Weakness :
Defect or characteristic that can lead to undesirable behavior
Vulnerability :
Weakness that can be exploited as part of an attack path
Cybersecurity information :
Information with regard to cybersecurity for which relevance is not yet determined
Cybersecurity incident :
Situation in the field that can involve vulnerability exploit mitigation
Triage :
Analysis to determine the relevance of cybersecurity information to an item or component

## Slide 80
LGE Internal Use Only
Cybersecurity incident response plan shall be created that includes :
  Remedial actions
    Remedial actions are determined by vulnerability management
Elimination
Of vulnerability by applying
available remediation (e.g. patch)
Vulnerability management TARA
Risk treatment
(until no unreasonable risk)
Vulnerability management tracks and oversees the treatment of identified vulnerabilities in items and components until their end of cybersecurity support
Communication plan
Assigned responsibilities for the remedial actions
Procedure for recording new cybersecurity information relevant to the cybersecurity incident
Method for determining progress
Criteria for closure of the cybersecurity incident response
Actions for the closure
Vulnerability analysis
Determine remediation actions

## Slide 81
LGE Internal Use Only
Update planning
  Update capabilities?
  Criticality categories?
  How & Where to deliver?
  Communicate end-of-support?
Recovery information (What if an update fails?)
  Testing of the update?
  Rollback options?
  Replace or repair?
  Was it successful?
UNECE R156 / ISO 24089

## Slide 82
LGE Internal Use Only

## Slide 83
LGE Internal Use Only
Objectives
  Communicate the end of cybersecurity support
  Enable decommissioning of items and components with regard to cybersecurity
Procedure shall be created to communicate to customers when an organization decides to end cybersecurity support for an
item or component
  These communications can be handled under contract requirements between suppliers and customers
  Communication to vehicle owners can be delivered by an announcement
Cybersecurity requirements for post-development with regard to decommissioning shall be available
  Appropriate documentation (e.g. instructions, user manuals) relating to such requirements can enable decommissioning with regard to cybersecurity

## Slide 84
LGE Internal Use Only
End of support
OEM production/ maintenance is stopped
Item/component can still function
No more updates
Supplier ends support of component
Decommissioning
Decommissioning occurs without organization’s knowledge
Decommissioning is out of control of OEM,
but should be considered through the product’s lifecycle
Under contract requirements between suppliers and customers
 Communication to vehicle owners by announcement

## Slide 85
LGE Internal Use Only
End of cybersecurity support and decommissioning shall be considered from the beginning of product development
Concept phase
Consideration :
Where are sensitive data stored?
Is it possible to delete the
memory?
How can item be reset?
How can we inform the car user how to delete data?
What communication channel shall be established?
…
Sec_Req_21:
All sensitive data including credit card numbers, GPS data, address book information and audio files shall be stored in the Memory Unit
Sec_Req_25:
Memory Unit shall have the capability to be reset
Risk analysis
If Risk assessment identifies that data cannot be fully deleted and the remaining risk is not acceptable, all sensitive data might be encrypted
Product development phase
Sec_Req_25_01:
Memory Unit shall be resettable by pushing the Power Button and the Volume up Button for 5 sec
Sec_Req_25_02:
Description how to reset Memory Unit shall be described in the User Manual
Adequate description in User Manual how to reset the
product is sufficient

## Slide 86
LGE Internal Use Only
ISO 21434 Analysis :
http://collab.lge.com/main/x/-a2bW